## Slide 1: OpenETCS project Summary of WP3 priorities concerning traceability
Meeting of 25 September 2015 + complements
Prepared by Raphael Faudou
(Samares Engineering)

## Slide 2: Key points summary
OpenETCS traceability process versus standard process
WP3 main priorites concerning traceability

## Slide 3: Standard SE process (ISO 15288:2015) without models
Stakeholders Needs
System requirements
SW building block requirements
Direct traceability
derive
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
System concepts (problem space)
System definition
(Solution definition)
Software block definition
And realization

## Slide 4: Standard SE process with models
System needs model
  UC / User Stories / Operational Scenarios
  Operational modes
System boundaries model
  System main functions
  Interface definitions
System Architecture Model
  Functional/logical architecture
  Physical configuration items
  Constraints/Equations
  Allocations
Stakeholders Needs
System requirements
SW building block Requirements
Direct traceability
Indirect traceability
through models
derive
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
SW Architecture Model
  Architecture / Design

## Slide 5: OpenETCS current process vs. standard
System boundaries model
  System main functions
  Interface definitions
System Architecture Model
  Functional/logical architecture
  Physical configuration items
  Constraints/Equations
  Allocations
Stakeholders Needs
System requirements
SW building block Requirements
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
SW Architecture Model
  Architecture / Design
SRS – Subset 26
User stories
OpenETCS function
formal model
reqID in comments area
code generator
Architecture and Design Document
Draft
User stories model
In sequence diagram
Cenelec EN50128
Data dictionnary model
Expected traceability (directly between requirements
or through models)
derive
OpenETCS architecture semi formal model

## Slide 6: OpenETCS current tooling context
System requirements
Current traceability
Derive
System level requirements
Decomposed and derived requirements
SRS – Subset 26
User stories
OpenETCS function Scade model
reqID in comments area
code generator
Architecture and Design Document
Draft
User stories model
In sequence diagram
Cenelec EN50128
Data dictionnary model
C code
OpenETCS architecture SysML model
Req gateway
Partially done

## Slide 7: WP3 priorities regarding traceability
Urgent: Scade model to SRS traceability
  Either through ReqTify tool
  Else (ideally) through open source solution
Nice to have: SysML model to SRS traeability
  Either through ReqIF/ReqCycle
  Else through other open source chain