## Slide 1: OpenETCS project Summary of WP3 priorities concerning traceability
Meeting of 25 September 2015 + complements
Prepared by Raphael Faudou
(Samares Engineering)

## Slide 2: Key points summary
OpenETCS traceability process versus standard process
WP3 main priorites concerning traceability

## Slide 5
UNISIG specifications
SRS – Subset 26
SW application executable code
Architecture and Design Document
(Draft)
Cenelec EN~50126-1:1999 and EN~50128:2011
National and Operational rules of operators
Experience of partners
ITEA 2 project application documents
ETCS track side equipment
Utrecht- Amsterdam track
OpenETCS architecture SysML model
User stories
Scope
SW Runtime System
openETCS API
OpenETCS (formal) executable SCADE
Model
Detailed design function model
Types model
Integration model
Reflect architecture
Functional block
integration
Generates (KCG)
Runtime API interface
Runtime API interface
Validation scenario
User stories model
produces
refinement
Input for

## Slide 6
Baseline of requirements
OpenETCS Software
Requirements
UNISIG specifications
SRS – Subset 26
Cenelec EN~50126-1:1999 and EN~50128:2011
National and Operational rules of operators
Experience of partners
ITEA 2 project application documents
ETCS track side equipment
Utrecht- Amsterdam reference track
User stories
Provides scope
openETCS API
User stories model
refinement
OpenETCS stakeholder
Reference requirements
OpenETCS product definition
Import reference requirements
OpenETCS System requirements
(including safety requirements)
Trace

## Slide 7
OpenETCS requirements
baseline
UNISIG specifications
SRS – Subset 26
Cenelec EN~50126-1:1999 and EN~50128:2011
National and Operational rules of operators
Experience of partners
ITEA 2 project application documents
ETCS track side equipment
Utrecht- Amsterdam reference track
User stories
openETCS API
User stories model
refinement
SRS Subset 26 requirements
as .ReqIF files matching chapters
OpenETCS product definition
Provides reference requirements
Translation
Translation
D2.6.9
Document format
Database format
Additional openETCS requirements as .reqIF files

## Slide 8: OpenETCS traceability priority
SRS – Subset 26
System architecture
(System + Subsystem + SW functions) SysML model
Generated SW code
openETCS derived and decomposed requirements
Traceability links to define and maintain (in current design process)
Traceability links automatically defined and maintained by generation
OpenETCS API
openETCS OBU formal executable (SW architecture + SW functions + detailed design) SCADE model
User stories

## Slide 9
Additional openETCS requirements
SRS Subset 26 requirements
as .ReqIF files
Requirement analysis
OpenETCS architecture SysML model - system level definition
OpenETCS product definition
External System Interfaces
External SW Interfaces
Deduce (create) requirements
System IF Req 1
SW Req 1
SW
Req 2
requirement creation at system level

## Slide 10
requirement creation at software level
OpenETCS architecture SysML model for system and SW architecture definition
OpenETCS Software
Requirements
OpenETCS (formal) overall executable SCADE Model
SW Integration model
Reflect architecture
Software level
requirements
Deduce (create) requirements
SW Component
Requirements
SW Component
Interface requirements
Input for
SRS Subset 26 requirements
as .ReqIF files

## Slide 11
requirement creation at software level
OpenETCS architecture SysML model - system level definition
OpenETCS product definition
OpenETCS Software
Requirements
OpenETCS (formal) executable SCADE
Model
Detailed design function model
Integration model
Reflect architecture
Functional block definition
integration
Types model
SW application executable code
Generates (KCG)
OpenETCS SW Architecture and Design Document (Draft)
Deduce (create) requirements
openETCS API
SRS Subset 26 requirements
as .ReqIF files
SW Component
Requirements
SW Component
Interface requirements
Software level
requirements
Input

## Slide 12
UNISIG specifications
SRS – Subset 26
SW application executable code
Architecture and Design Document
(Draft)
Cenelec EN~50126-1:1999 and EN~50128:2011
National and Operational rules of operators
Experience of partners
ITEA 2 project application documents
ETCS track side equipment
Utrecht- Amsterdam reference track
OpenETCS architecture SysML model
User stories
Provides scope
SW Runtime System
openETCS API
OpenETCS (formal) executable SCADE
Model
Detailed design function model
Types model
Integration model
Reflect architecture
Functional block
integration
Generates (KCG)
Runtime API interface
Runtime API interface
Validation scenario
User stories model
produces
refinement
implements
Satisfies
Validated by
Satisfies

## Slide 13
Architecture
Model (SysML)
OBU integration Executable formal
Model (SCADE)
F2.1
F2.2
F2.3
F2.15
Functional design model
Operational environment
model (SCADE)

## Slide 14: WP3 priorities regarding traceability
Urgent: Scade model to SRS traceability
  Either through ReqTify tool
  Else (ideally) through open source solution
Nice to have: SysML model to SRS traeability
  Either through ReqIF/ReqCycle
  Else through other open source chain

## Slide 15: 2nd solution – ProR + ReqCycle
Reference Requirement Data Base
RT-tester
4. Copy (to support traceability)
Subset 026
ReqCycle
SCADE
Papyrus
5. Link
5. Link
Read Only Requirement Data Base
3. Update
1. Import
OpenETCS API
2. Import
ProR
GenDoc
7. export
6. Create tests
manage

## Slide 16: Reqcycle – prepare trace link with SCADE
Generate requirement traceability annotation for external element
Copies traceability string annotation (ReqID + Satisfy ID) to clipboard

## Slide 17: 3rd solution – ReqCycle only
RT-tester
1.A Import
Subset 026
ReqCycle
SCADE
Papyrus
Link
Link
Reference Requirement Data Base
Update
Subset 026 requirements
1.B1 Import
1.B2 Import
OpenETCS API
2. Import
GenDoc
7. export

## Slide 18: OpenETCS current tooling context
System requirements
Current traceability
Derive
System level requirements
Decomposed and derived requirements
SRS – Subset 26
User stories
OpenETCS function Scade model
reqID in comments area
code generator
Architecture and Design Document
Draft
User stories model
In sequence diagram
Cenelec EN50128
Data dictionnary model
C code
OpenETCS architecture SysML model
Req gateway
Partially done

## Slide 19: BACKUP

## Slide 21
System other needs/inputs
Software design
(SW components)
subsystem level definition
SW needs
SS other needs/inputs
System and project context: standards, reference and background material
System (ETCS)
definition
Cenelec EN~50126-1:1999
Elaborated SRS
(relevant for project)
SW level definition
Subsystem requirements
Subsystem Safety specification
SubSystem
architecture design specification
SW Requirements
(including safety requirements)
National and Operational rules of operators
Experience of partners
UNISIG– Subset 26
SW architecture design specification
System architecture design specification
Input for
OpenETCS Background
Domain/project
specifications
Needs/requirements defined by project
UNISIG specifications
Cenelec EN~50128:2011
ITEA 2 project application documents
Hazard & Risks
ETCS track side equipment
Plans
Safety Plan
Acceptance
Plan
QA plan
Validation plan
SW Overall Test Specification
Verification
plan
HW API
SW Interface Specification
SW Integration Test Specification
Plans defined by project
OpenETCS API
Standard Engineering
requirements
Hazard & Risks

## Slide 22: 3 generic Systems engineering levels
System leaf element can be software, hardware, data or procedure
Stakeholders Needs
System-of-interest (SoI) requirements
Subsystem 1
Stakeholder
requirements
Stakeholders
requirements
System-of-interest problem definition
System-of-interest
Solution definition
(system and subsystems recursive definition)
System leaf Element stakeholder requirements
Subsystem 2
Stakeholder requirements
Subsystem 2.1
requirements
Subsystem 2.2 requirements
Element
requirements
Trace
Transformed into
Other needs for SoI
System-of-interest leaf element definition
(lowest definition level)
Other needs for Subsystem 2
Other needs for elements
To be continued (recursive)
To be continued (recursive)
Element requirements
Subsystem 2 leaf element stakeholder requirements
Subsystem 2
requirements

## Slide 24: Standard SE process with models
System needs model
  UC / User Stories / Operational Scenarios
  Operational modes
System boundaries model
  System main functions
  Interface definitions
System Architecture Model
  Functional/logical architecture
  Physical configuration items
  Constraints/Equations
  Allocations
Stakeholders Needs
System requirements
SW building block Requirements
Traceability (between requirements or through models)
derive
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
SW Architecture Model
  Architecture / Design

## Slide 25: OpenETCS current process vs. standard
System needs model
  UC / User Stories / Operational Scenarios
  Operational modes
System boundaries model
  System main functions
  Interface definitions
System Architecture Model
  Functional/logical architecture
  Physical configuration items
  Constraints/Equations
  Allocations
Stakeholders Needs
System requirements
SW building block Requirements
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
SW Architecture Model
  Architecture / Design
SRS – Subset 26
User stories
OpenETCS function
(formal) model
reqID in comments area
code generator
Architecture and Design Document
Draft
User stories model
Cenelec EN50128
Data dictionnary model
OpenETCS architecture (semi formal) model
Direct traceability
Indirect traceability
through models
derive

## Slide 26
OpenETCS Software
Requirements
UNISIG specifications
SRS – Subset 26
Cenelec EN~50126-1:1999 and EN~50128:2011
National and Operational rules of operators
Experience of partners
ITEA 2 project application documents
ETCS track side equipment
Utrecht- Amsterdam reference track
User stories
Provides scope
openETCS API
User stories model
refinement
OpenETCS stakeholder
reference (baselined) requirements
OpenETCS product definition
Provides reference requirements
OpenETCS System Requirements
Subsystem level
System level
Software level
Component level
Trace

## Slide 27
Summary of requirement creation
OpenETCS architecture SysML model - system level definition
OpenETCS product definition
OpenETCS Software
Requirements
Software level
OpenETCS System
Requirements
Subsystem level
System level
Deduce (create) requirements
OpenETCS stakeholder
reference (baselined) requirements
Requirement analysis

## Slide 28
OpenETCS architecture SysML model - system level definition
OpenETCS System requirements
OpenETCS product definition
External IF
System level
Subsystem level
External IF
Deduce (create) requirements
requirement creation at system level

## Slide 29
UNISIG specifications
SRS – Subset 26
Cenelec EN~50126-1:1999 and EN~50128:2011
National and Operational rules of operators
Experience of partners
ITEA 2 project application documents
ETCS track side equipment
Utrecht- Amsterdam reference track
User stories
Provides scope
openETCS API
User stories model
refinement
OpenETCS stakeholder
reference (baselined) requirements
OpenETCS product definition
Deduce (create) requirements

## Slide 30: OpenETCS traceability priority
SRS – Subset 26
System architecture
(system + SW) SysML model
Generated SW code
openETCS derived and decomposed requirements
Traceability links to define and maintain in “full process”
Traceability links automatically defined and maintained by generation
OpenETCS API
openETCS OBU formal executable (SW architecture + SW functions + detailed design) SCADE model
User stories

## Slide 31
requirement creation at system level
Requirement analysis
OpenETCS architecture SysML model - system level definition
OpenETCS System requirements
OpenETCS product definition
External System Interfaces
External SW Interfaces
Deduce (create) requirements
OpenETCS Software
Requirements
OpenETCS stakeholder
reference (baselined) requirements
Trace

## Slide 32
Additional openETCS requirements
SRS Subset 26 requirements
as .ReqIF files
Requirement analysis
OpenETCS architecture SysML model - system level definition
OpenETCS product definition
External System Interfaces
External SW Interfaces
Deduce (create) requirements
System IF Req 1
SW IF Req 1
SW IF
Req 2
requirement creation at system level

## Slide 33
OpenETCS architecture SysML model - system level definition
OpenETCS product definition
OpenETCS Software
Requirements
OpenETCS (formal) executable SCADE
Model
Detailed design function model
Integration model
Reflect architecture
Functional block
integration
Software level
Component
level
Types model
SW application executable code
Generates (KCG)
OpenETCS SW Architecture and Design Document (Draft)
System functions and Internal IF
Deduce (create) requirements
requirement creation at software level

## Slide 34
OpenETCS architecture SysML model - system level definition
OpenETCS product definition
OpenETCS (formal) executable SCADE
Model
Detailed design function model
Integration model
Reflect architecture
Functional block
integration
OpenETCS Software
Requirements
Software level
Component
level
Types model
SW application executable code
Generates (KCG)
OpenETCS SW Architecture and Design Document (Draft)
OpenETCS System
Requirements
Subsystem level
System level
Deduce (create) requirements
Summary of requirement creation