## Slide 1: OpenETCS project Summary of WP3 priorities concerning traceability
Meeting of 25 September 2015 + complements
Prepared by Raphael Faudou
(Samares Engineering)

## Slide 2: Key points summary
OpenETCS traceability process versus standard process
WP3 main priorites concerning traceability

## Slide 3: Standard SE process (ISO 15288:2015) without models
Stakeholders Needs
System requirements
SW building block requirements
Direct traceability
derive
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
System concepts (problem space)
System definition
(Solution definition)
Software or hardware block definition and realization

## Slide 4: OpenETCS requirements with regards to ISO 15288:2015 engineering levels
Stakeholders Needs
System requirements
SW building block requirements
Direct traceability
derive
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
System concepts (problem space)
System definition
(Solution definition)
Software block definition
And realization
SRS – Subset 26
User stories
Cenelec EN 50128
openETCS decomposed and derived requirements
OpenETCS API

## Slide 5: Standard SE process with models
System needs model
  UC / User Stories / Operational Scenarios
  Operational modes
System boundaries model
  System main functions
  Interface definitions
System Architecture Model
  Functional/logical architecture
  Physical configuration items
  Constraints/Equations
  Allocations
Stakeholders Needs
System requirements
SW building block Requirements
Traceability (between requirements or through models)
derive
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
SW Architecture Model
  Architecture / Design

## Slide 6: OpenETCS current process vs. standard
System needs model
  UC / User Stories / Operational Scenarios
  Operational modes
System boundaries model
  System main functions
  Interface definitions
System Architecture Model
  Functional/logical architecture
  Physical configuration items
  Constraints/Equations
  Allocations
Stakeholders Needs
System requirements
SW building block Requirements
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
SW Architecture Model
  Architecture / Design
SRS – Subset 26
User stories
openETCS OnBoard Unit functions
(executable) model
Cenelec EN50128
Architecture
(semi formal) model
Data dictionnary model
User stories model
Traceability (between requirements or through models)
derive
openETCS decomposed and derived requirements
OpenETCS API

## Slide 7: WP3 priorities regarding traceability
Urgent: Scade model to SRS traceability
  Either through ReqTify tool
  Else (ideally) through open source solution
Nice to have: SysML model to SRS traeability
  Either through ReqIF/ReqCycle
  Else through other open source chain

## Slide 8: OpenETCS traceability priority
SRS – Subset 26
System architecture
(semi formal) model
Data dictionnary model
openETCS OBU functional
(formal)
executable model
Generated SW code
openETCS decomposed and derived requirements
Traceability links to define and maintain
Traceability links automatically defined and maintained by generation
OpenETCS API

## Slide 9: 2nd solution – ProR + ReqCycle
Reference Requirement Data Base
RT-tester
4. Copy (to support traceability)
Subset 026
ReqCycle
SCADE
Papyrus
5. Link
5. Link
Read Only Requirement Data Base
3. Update
1. Import
OpenETCS API
2. Import
ProR
GenDoc
7. export
6. Create tests
manage

## Slide 10: Reqcycle – prepare trace link with SCADE
Generate requirement traceability annotation for external element
Copies traceability string annotation (ReqID + Satisfy ID) to clipboard

## Slide 11: 3rd solution – ReqCycle only
RT-tester
1.A Import
Subset 026
ReqCycle
SCADE
Papyrus
Link
Link
Reference Requirement Data Base
Update
Subset 026 requirements
1.B1 Import
1.B2 Import
OpenETCS API
2. Import
GenDoc
7. export

## Slide 12: OpenETCS current tooling context
System requirements
Current traceability
Derive
System level requirements
Decomposed and derived requirements
SRS – Subset 26
User stories
OpenETCS function Scade model
reqID in comments area
code generator
Architecture and Design Document
Draft
User stories model
In sequence diagram
Cenelec EN50128
Data dictionnary model
C code
OpenETCS architecture SysML model
Req gateway
Partially done

## Slide 13: BACKUP

## Slide 14: OpenETCS current process vs. standard
System needs model
  UC / User Stories / Operational Scenarios
  Operational modes
System boundaries model
  System main functions
  Interface definitions
System Architecture Model
  Functional/logical architecture
  Physical configuration items
  Constraints/Equations
  Allocations
Stakeholders Needs
System requirements
SW building block Requirements
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
SW Architecture Model
  Architecture / Design
SRS – Subset 26
User stories
OpenETCS function
(formal) model
code generator
Architecture and Design Document
Draft
User stories model
Cenelec EN50128
Data dictionnary model
OpenETCS architecture (semi formal) model
Direct traceability
Indirect traceability
through models
derive

## Slide 15: OpenETCS current process vs. standard
System needs model
  UC / User Stories / Operational Scenarios
  Operational modes
System boundaries model
  System main functions
  Interface definitions
System Architecture Model
  Functional/logical architecture
  Physical configuration items
  Constraints/Equations
  Allocations
Stakeholders Needs
System requirements
SW building block Requirements
System level requirements
Decomposed and derived requirements
Stakeholders
requirements
SW low-level requirements
SW Code
SW Architecture Model
  Architecture / Design
SRS – Subset 26
User stories
OpenETCS function
(formal) model
reqID in comments area
code generator
Architecture and Design Document
Draft
User stories model
Cenelec EN50128
Data dictionnary model
OpenETCS architecture (semi formal) model
Direct traceability
Indirect traceability
through models
derive