## Slide 1: openETCS project ReqCycle support for traceability between .reqIF and Papyrus SysML
V1.2 – 21st of November 2015
Raphael Faudou

## Slide 2: Agenda
ReqCycle installation with patches for bugs 625, 626, 627 and 642
Setup of openETCS ReqCycle configuration
Tutorial to create and remove links with chapter4. reqIF
Export/import of traeability
Current limits

## Slide 3: 1. ReqCycle installation

## Slide 4: ReqCycle 0.8.0 openETCS installation
Download openETCS ReqCycle patched installation:
  https://github.com/openETCS/toolchain/raw/master/tool/reqcycle-update-site-0.8.0
  In Eclipse, go to menu Help>Install new software...
On the top area, click "Add" button to add a repository.
Set "ReqCycle OpenETCS update site" as name, click « archive » button and select downloaded .zip file (step 1)
Click Next until the end of wizard (Finish).
Restart Eclipse platform as requested by wizard.
That' it: ReqCycle is installed. You can check that installation is OK by looking at "ReqCycle" perspective and selecting it.

## Slide 5: openETCS reqCycle configuration

## Slide 6: Setup ReqCycle openETCS configuration
Launch Eclipse and open « ReqCycle » perspective
Two options
  Fast but opaque: import openETCS configuration file (easier but less explanation - already done for you – cannot modify it, just extend it). See next slide to perform import – presentation of configuration is shown in slides 8 and 9
  Create your own configuration: explained step by step in ReqCycle wiki tutorial available here:https://polarsys.org/wiki/Model_Based_System_Engineering_tutorial_with_ATM_system

## Slide 7: Import configuration file
Go to « ReqCycle » top menu and select « initialize configuration »
Say OK and select « openETCSReqCycle-Conf.zip »
  Restart, that’s it

## Slide 8: ReqCycle OpenETCS illustrated configuration
5 scopes created
but only SRS will be used to manage Subset 26
Attributes reflect ReqIF attributes
+ fullCovered specific attribute

## Slide 9: ReqCycle OpenETCS illustrated configuration
Traceability link type defined to support architecture verification: beween a requirement anda a model element

## Slide 10: Creation of traceability links
Quick openETCS Tutorial in next slides
Full tutorial on wiki:
https://polarsys.org/wiki/Step_2:_import_or_reference_system_requirements
https://polarsys.org/wiki/Step_3:_refine_system_requirements_through_a_SysML_model

## Slide 11: Initialize Eclipse projects
Launch Eclipse platform, choose a workpace (for instance « openETCS »)
Open ReqCycle perspective
Create « Reference requirements » general project.
Copy/paste .reqIF SRS chapter files in project
Then create another Eclipse general project for model
Import (or copy/paste) SysML model files

## Slide 12: Goto « Requirement sources view » and create ReqIF requirement source for chapter3 by following tutorial (below and next slides) To do for all other chapters
Avoid special characters in name: « - » is OK but other ones might raise bugs

## Slide 13: Import of chapter3.reqIF – mapping with custom data model (select both elements and map)

## Slide 14: Load requirement view with requirement source (click on « database » icon and select chapter you want to trace) and then expand nodes

## Slide 15: Examples of links to create

## Slide 16: Load ETCS papyrus SysML model (in project explorer view, double click on openETCS_EVC element with Papyrus icon) and click « cancel » on the first popup windows that is displayed about missing profiles (we do not care of missing Scade profiles for now)

## Slide 17: Create trace link through DnD

## Slide 18: Or create trace link through traceability creator view (select source, click +, select target, click + and click arrow)

## Slide 19: See traceability in ReqCycle with traceability table view (click « all links » and « refresh »)
Can filter results by a string...

## Slide 20: Remove links
Removal of links can only be done by end user from traceability table in « transverse links » mode
  Click « transverse links » and select the models Eclipse project (where you put the SysML model) : it contains the traceability.rdf hidden file with links.
  Right click on link to delete, a popup menu shows

## Slide 21: Use « properties » view to adapt « FullyCovered » req attribute
Note: cannot change ID nor text

## Slide 22: Export traceability with File>export...>Reqcycle>xls and csv

## Slide 23: File>export...>Reqcycle>xls and csv, check workspace, choose.csv and choose a directory, then click finish

## Slide 24: Finish export and open .csv Links are available with target element

## Slide 25: Export and import of traceability data

## Slide 26: Export and import configuration, requirements and traceability
Go to top menu ReqCycle
  Select export configuration
  Select « requirement sources »
  Click ok: a .zip file is created
Do not forget to export projects
  requirement project owns .reqCycle files that contain requirement in reqcycle format
  Models project owns .traceability.rdf file (hidden) that contains traceability data
On another computer with ReqCycle installed, first import projects and then import exported configuration zip file (through ReqCycle top menu) to get req data model and req sources and traceability data.

## Slide 27: Current limits

## Slide 28: Not yet support for concurrent work in ReqCycle
See export/import feature previously
  One can create links and then export work
  Another one can then import projects and ReqCycle configuration and continue work
But if two people work concurrently, it is not yet possible to merge traceability results in ReqCycle
  But can be done in Excel after concurrent exports...

## Slide 29: Advanced features

## Slide 30: Following of traceability progress in ReqCycle

## Slide 31: Can use a custom visualization to highlight already traced requirements and those that are fully covered
Can be done through custom visualization
Tutorial to provide if needed

## Slide 32: Questions?